## Slide 1
S. Assadi, J. Kellams, P. McIntyre,
K. Melconian, N. Pogue, and A. Sattarov
Texas A&M University
Strong-Focusing Cyclotron:
FFAG for High Current Applications
Notes: Total 15 min, plan 12-13. Turn in day before talk

## Slide 2: Outline
Motivation
  Proton driver for Accelerator-Driven Subcritical Fission
  What limits beam current in cyclotrons?
Superconducting RF Cavity
  Fully separate all orbits
  Distributed coupling to match beam loading
Beam Transport Channel
  Control betatron tunes throughout acceleration
  Magnetic design
  Winding prototype
Sector Dipoles
  Flux-coupled stack
  Fringe field reduction
Beam Dynamics

## Slide 3: FFAG is typically configured to accelerate a large momentum admittance within a modest magnet aperture.
1 GeV CW FFAG for C Therapy
C. Johnstone – Trinity College, 2011
3 to 10 GeV muon double beam FFAG
T. Planche - Nufact09
They are brilliant designs, as long as you don’t want too much beam current…

## Slide 4: Accelerator Driven Molten Salt System
Destroy long lived nuclear waste
Close nuclear fuel cycle
Subcritical - Safe
Produce power
TAMU 800
TAMU 100

## Slide 5: Current limits in cyclotrons: 1) Overlapping bunches in successive orbits
Overlap of N bunches on successive orbits produces N x greater space charge tune shift,
non-linear effects at edges of overlap.
http://cas.web.cern.ch/cas/Bilbao-2011/Lectures/Seidel.pdf
Radius (in)
# particles
http://www.nscl.msu.edu/~marti/publications/beamdynamics_ganil_98/beamdynamics_final.pdf

## Slide 6: 2) Weak focusing, Resonance crossing
Cyclotrons are intrinsically weak-focusing accelerators
Rely upon fringe fields
Low tune requires larger aperture
Tune evolves during acceleration
Crosses resonances
Scaling, Non-scaling FFAG utilize non-linear fields
Rich spectrum of unstable fixed pts
PSI
Space charge shifts, broadens resonances, feeds synchro-betatron
Even if a low-charge bunch accelerates smoothly, a high-charge bunch may undergo breakup even during rapid acceleration

## Slide 7: Strong-Focusing Cyclotron
Curing the limits of overlapping orbits and controlling tunes opens the high-current frontier:
Proton driver for ADS fission
Medical Isotope Production
Ion beam therapy
Muon Cooling
Completely separate all orbits.
Put beam transport channels in each sector to control betatron tunes

## Slide 8: SFC Components
SRF Cavities
Beam Transport Channels
Cold-Iron Pole Piece
Warm Flux Return
Warm Shielding Fins
Sectors are simple radial wedges – optimum for integrating SRF

## Slide 9: TRITRON was the first to attempt to make a separated orbit cyclotron
The good-field fraction of radial aperture was <50% for each orbit, so admittance was limited.
The intervening years of superferric magnet technology (and now MgB2) and Nb cavity technology make this a fertile time to make a strong-focusing cyclotron for high current.
Energy gain in its superconducting Pb cavities was limited by multipacting.

## Slide 10: Outline
Motivation
  Proton driver for Accelerator-Driven Subcritical Fission
  What limits beam current in cyclotrons
Superconducting RF Cavity Fully separate all orbits
Beam Transport Channel
  Control betatron tunes throughout acceleration
  Magnetic design
  Winding prototype
Sector Dipoles
  Flux-coupled stack
  Fringe field reduction
Beam Dynamics
Future Work

## Slide 11: Slot-geometry ¼-wave SRF Cavities
Superconducting RF cavities
100 MHz
2 MV/cavity energy gain
20 MV/turn fully separates orbits

## Slide 12: Example SRF Cavity Model
21 MV/m max surface electric field
54 mT max surface magnetic field
- less than design fields on SRF cavities for BNL, FRIB

## Slide 13: Slot-geometry ¼ wave cavity structure and distributed RF drive suppresses perturbations from wake fields
RF power is coupled to the cavity by rows of input couplers along the top/bottom lobes.
RF power is coupled from the cavity to the synchronous bunches traversing the slot gap.
The cavity serves as a linear transformer.
Its geometry accommodates transverse mode suppression
Energy coupled in
Energy coupled out

## Slide 14: Linear coupler array to match drive to beam loading, convolutes to suppress multipacting
Distributed drive matches to distributed beam loading for stability under high beam loading.
Note: this requires that all orbits are made very close to isochronicity…
Each coupler driven by solid state amplifier

## Slide 15: Outline
Motivation
  Proton driver for Accelerator-Driven Subcritical Fission
  What limits beam current in cyclotrons
Superconducting RF Cavity Fully separate all orbits
Beam Transport Channel
  Control betatron tunes throughout acceleration
  Magnetic design
  Winding prototype
Sector Dipoles
  Flux-coupled stack
  Fringe field reduction
Beam Dynamics
Future Work

## Slide 16: Sector dipoles - Flux-Coupled Stack
Beam Planes
Levitated-pole design originated at Riken
Common warm-iron flux return
Each gap formed by a pair of cold-iron flux plates
Multiple SFCs in single footprint
~1 T dipole field, isochronous B(r)
Geometric wedges (optimum for rf)

## Slide 17: Sector Dipole Modeling
1.8
1.6
1.4
1.2
1
0.8
0.6
0.4
0.2
Mid-plane magnetic flux density (T)
Top half of single stack cyclotron for modeling

## Slide 18: Fringe Field Reduction
Superconducting cavities require the magnetic flux density to be less than 40 mT 10 cm from the warm iron flux return.
Cold iron pole piece
Warm-iron flux return
Fringe field suppression
MgB2 main windings
Levitated pole method first pioneered at Riken
mT mT

## Slide 19: Outline
Motivation
  Proton driver for Accelerator-Driven Subcritical Fission
  What limits beam current in cyclotrons
Superconducting RF Cavity Fully separate all orbits
Beam Transport Channel
  Control betatron tunes throughout acceleration
  Magnetic design
  Winding prototype
Sector Dipoles
  Flux-coupled stack
  Fringe field reduction
Beam Dynamics
Future Work

## Slide 20: F-D doublet on each orbit, each sector
BTC dimension set by beam separation at extraction
>80% of horizontal aperture is useful for orbits.
5.6cm
F
D

## Slide 21: Beam Transport Channel (BTC)
Dipole Windings
Up to 20 mT
Act as corrector for isochronicity,
Septum for injection/extraction
Quadrupole Windings
Up to 6 T/m
Panofsky style
Alternating-gradient focusing
Powered in 6 families to provide total tune control

## Slide 22: All BTC windings use MgB2
Operate with 15-20 K refrigeration cycle
10 x less AC power to refrigerate,
50 x more heat capacity compared to NbTi @ 4.2 K

## Slide 23: 2D Field Modeling
Wire spacing adjusted to kill multipoles
Current density required for 6T/m ~ 235 A
T
Cold iron pole piece
Notes: Using dimensions set by orbit spacing need superconductor, image with external dipole suppressed.

## Slide 24: F-D quads control betatron motion
We can lock nx, ny to any desired operating point.
BTC quads are tuned in 2 x 5 families.
Sextupole correctors at exit of each BTC are tuned in 2 x 6 families.
First 2 turns each have dedicated families so that they can be tuned first for rational commissioning.
0.0 0.5 1.0 1.5 2.0 2.5
5.5
5.0
4.5
4.0
Uniform gradient in each channel: excellent linear dynamics.

## Slide 25: We have developed a simulation platform that takes high-current bunches through the spiral orbit, treating it as a spiral transfer line.
Elegant
Hyper_TAMU, MPI_TAMU
Later
No access
No access
Later
Accounts for details of 6-D dynamics:
resonance dynamics,
synchro-betatron couplings,
space charge,
wake fields
beam loading

## Slide 26: Coordinates, Mesh, Global coordinates, Beam assumptions…

## Slide 27: Equations of motion are nonlinear, coupled, damped:
The code enables us to make a self-consistent solution for B(r); RF DE(r) and f(r), BTC gradients, BTC trim dipoles, sextupoles to simultaneously provide isochronicity, constant tunes, stable phase advances.
It then tracks, generates Poincare plots, etc for desired bunch properties.

## Slide 29: Dipole Corrector
The BTC dipole correctors are used to maintain isochronicity and locally manage beam spacing at injection, extraction.
Example of ability to adjust orbits to optimize design (from a 6 sector 100 MeV SFC design):
Design orbits working in from extraction:
First try gave problematic orbits @ injection
Then adjust orbit pattern using dipole correctors – ideal accommodation for injection

## Slide 30: We are now modeling 6-D transport through the SFC including effects of x/y coupling, synchrobetatron, and space charge
300k particle simulation

## Slide 31: Charge Density for 10 mA beam
Longitudinal charge distribution
20k particle
2K particles
20K particles

## Slide 32: Matched optics from injection to extraction. Left pictures shows how a bunch transfers from one sector To another.
head tail
Plots of slice energy spread and b mismatch after first turn, sensitive to bunch length – no hourglass from synchrobetatron
I s
radial E from space charge inside bunch
10 mA beam, ± 5o total phase width

## Slide 33: Effect of ±.3 MeV energy mismatch on a bunch injected at 9 MeV
bunch is clumping after half-turn (after 2 cavities)

## Slide 34: Longitudinal line charges along a bunch - 10 mA beam, injected at 9 MeV.
Distortion in distribution comes from the space charge
After first cavity just before extraction
Radial E from space charge

## Slide 35: Accelerating bunch at injection, extraction
100 MeV
9 MeV
Axial E from space charge

## Slide 36: Longitudinal phase space with 10 mA
9 MeV injection 100 MeV extraction
±5o phase width ±6o phase width
Energy width increases ~30%. Sextupole correction at exit from each BTC
(2 x 6 families)

## Slide 37: Transverse phase space of 10 mA bunch through acceleration:
x/y profile
Vertical Emittance
Horizontal Emittance
First at injection:

## Slide 38: Now look at effects of synchrobetatron and space charge with 10 mA at extraction:
1/3 order integer effect
1/5 order integer effect
1/5-order islands stay clumped, 1/3-order islands are being driven. Likely driving term is edge fields of sectors (6-fold sector geometry). We are evaluating use of sextupoles at sector edges to suppress growth.
Move tunes near integer fraction resonances to observe growth of islands
After two turns … bunch is lost by 20 MeV

## Slide 39: Synchrobetatron/space charge in longitudinal phase space:
Injection extraction
Phase width grows x5 at extraction
Tunes again moved to approach resonances, but retaining transmission through lattice

## Slide 40: Poincare Plots of 5 s contours
Injection 40 MeV Extraction
3.5 mA
beam
Now change the tune to excite a 7th order resonance
An example favorable operating point: (nx, ny) = (3.196, 3.241)

## Slide 41: Conclusions
The strong-focusing cyclotron is a new member of the FFAG family.
It is optimized to accelerate the highest possible CW beam current with low losses and high energy efficiency.
We have validated the capability of the design to accelerate 10 mA with excellent transport.
Control of betatron tunes and ability to naturally match input RF to beam loading across the entire width of the spiral orbit are key strategic elements.
Phase space dynamics for optimized orbit should be simple to diagnose – no COD, no E-f serpentine, no resonances
Anyone who can tune a synchrotron or linac for low loss, high current could tune a SFC.
So far as we can determine from these early studies, it is not yet clear what will be the ultimate limits to beam current.

## Slide 42: Future plans
To Do:
  SRF cavity
  Wake fields, beam loading, optimize input coupler array
  Build/test prototype cavities
  Beam Transport Channel:
  Finalize copper test wind
  Quench modeling and protection
  MgB2 winding
  Sector Magnet
  Refine pole piece and shielding fins - FEA models and prototypes
  Beam dynamics
  Model beam loading, wake fields, patterns of input couples in SRF cavities

## Slide 43
Come collaborate with us!
Thank you!